## Slide 1: Wireless IOT 2IOT
Lora Lab RPI

## Slide 2: The Things Network
The Things Network is about enabling low power Devices to use long range Gateways to connect to an open-source, decentralized Network to exchange data with Applications.

## Slide 3: LoRa: Properties

## Slide 4: Devices and Gateways
TCP/IP
TCP/IP
TCP/IP
Client
(PC)
Arduino MKR WAN 1310
RPi + RFM95W
TCP/IP
TCP/IP
TTN Indoor Gateway (8ch)
RPi + Dragino Gateway (1ch)
Server
(cloud)
TCP/IP

## Slide 5: Setup: RPi, Analog in, LM35, MCP3008, RFM95W LoRa

## Slide 6: Preparations (details see next slides)
Install RFM95W on RPi:
  CircuitPython (Blinka), SPI, TinyLoRa
Create an account on TTN: link
Register a device on TTN: link
  Use ABP: Activation By Personalization
Find keys to use in Python code:
  Device Address, Network Session Key, App Session Key
Run code (see further) on RPi and check data
Decode payload:

## Slide 7: Decoder
// TinyLoRa Decoder
function Decoder(bytes, port) {
var decoded = {};
// Decode bytes to int
var voltInt = (bytes[0] << 8) | bytes[1];
var tempInt = (bytes[2] << 8) | bytes[3];
// Decode int to float
decoded.volt = voltInt / 100;
decoded.temp = tempInt / 100;
return {
field1: decoded.volt,
field2: decoded.temp
}
}

## Slide 8: Update your Pi and Python
Run the standard updates:
    sudo apt-get update
    sudo apt-get upgrade (probably not necessary on a fresh image, can take a lot of time)
    sudo pip3 install --upgrade setuptools
If above doesn't work try
    sudo apt-get install python3-pip
Notes: On Pi5: create virtual environment
sudo apt install python3-venv
python3 -m venv blinka-env --system-site-packages
source blinka-env/bin/activate
(deactivate)

## Slide 9: Enable SPI
Run raspi-config and enable SPI
    sudo raspi-config
Once SPI enabled, verify you have the SPI devices with the command
    ls /dev/spi*
You should see the response
    /dev/spidev0.0 /dev/spidev0.1

## Slide 10: Install Python libraries
Run the following command to install adafruit_blinka (CircuitPython)
    pip3 install adafruit-blinka
The computer will install a few different libraries such as adafruit-pureio (our ioctl-only i2c library), spidev (for SPI interfacing), Adafruit-GPIO (for detecting your board) and of course adafruit-blinka

## Slide 11: Install required CircuitPython Libraries
Run the following command from your terminal to install the Adafruit_CircuitPython_TinyLoRa library to communicate with the RFM9x breakout board
    sudo pip3 install adafruit-circuitpython-tinylora==2.2.6

## Slide 12: Python code: TTN transmitter
Install, configure (keys) and run the TTN transmitter Python program

## Slide 13: Python code: TTN transmitter
import time
import RPi.GPIO as GPIO
import busio
import digitalio
import board
from adafruit_bus_device.spi_device import SPIDevice
from adafruit_tinylora.adafruit_tinylora import TTN, TinyLoRa
interval = 15 # Sample period in seconds
GPIO.setmode(GPIO.BCM) # use GPIO numbers
# Initialize SPI bus
spi = busio.SPI(board.SCK, MOSI=board.MOSI, MISO=board.MISO)
# Initialize control pins for adc
cs0 = digitalio.DigitalInOut(board.CE0) # chip select CE0 for adc; alternatively use e.g. Dxx (=GPIOxx)
adc = SPIDevice(spi, cs0, baudrate= 1000000)
# RFM9x Breakout Pinouts
cs = digitalio.DigitalInOut(board.D5)
irq = digitalio.DigitalInOut(board.D6)
rst = digitalio.DigitalInOut(board.D4)
# TTN Device Address, 4 Bytes, MSB
devaddr = bytearray([0x00, 0x00, 0x00, 0x00])
# TTN Network Key, 16 Bytes, MSB
nwkey = bytearray([0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00])
# TTN Application Key, 16 Bytess, MSB
app = bytearray([0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00])
ttn_config = TTN(devaddr, nwkey, app, country='EU')
lora = TinyLoRa(spi, cs, irq, rst, ttn_config, channel=0)
# Data Packet to send to TTN
data = bytearray(4)
# read SPI data 8 possible adc's (0 thru 7)
def readadc(adcnum):
if ((adcnum > 7) or (adcnum < 0)):
return -1
with adc:
r = bytearray(3)
spi.write_readinto([1,(8+adcnum)<<4,0], r)
time.sleep(0.000005)
adcout = ((r[1]&3) << 8) + r[2]
return adcout
# Run until you get a ctrl^c
try:
while True:
tmp0 = readadc(0) # read channel 0
tmp1 = readadc(1) # read channel 1
volt_val = 3.3*tmp0/1024 # potmeter at ch0
temp_val = 100*3.3*tmp1/1024 # LM35 at ch1
# Print for debugging, uncomment the below line
print("Voltage: %4.2f, Temperature: %4.2f" % (volt_val, temp_val))
# Encode float as int
volt_val = int(volt_val * 100)
temp_val = int(temp_val * 100)
# Encode payload as bytes
data[0] = (volt_val >> 8) & 0xff
data[1] = volt_val & 0xff
data[2] = (temp_val >> 8) & 0xff
data[3] = temp_val & 0xff
# Send data packet
print('Sending packet...')
lora.send_data(data, len(data), lora.frame_counter)
print('Packet Sent!')
lora.frame_counter += 1
time.sleep(interval)
except KeyboardInterrupt:
pass

## Slide 14: Create an application

## Slide 15: Create an end device

## Slide 16: End device Network layer
Use reset to receive data after making changes

## Slide 17: End device Advanced MAC settings

## Slide 18: ThingSpeak TTN integration
ThingSpeak: https://thingspeak.com/
ThingSpeak - integrations: https://www.thethingsindustries.com/docs/integrations/

## Slide 19: ThingSpeak TTN integration